## Slide 1: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
http://www.ipcomms.net/asteriskblog/1-11-steps-to-secure-your-asterisk-pbx

## Slide 2: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
1. Identify critical assets (& asset owner)
2. Research on applicable security controls
3. Checklist of applicable controls
5. Implement controls on test setup
4. Document controls into SOP
6. Validation of control implementation
7. Change management process for PROD
8. Implement on PROD & monitor

## Slide 3: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
7. Limit registration by extensions to your local subnet.
Restrict the IP addresses your extensions can register onto the local subnet. Asterisk PBXs can use the ACL (permit/deny) in SIP.conf to block IP addresses. This can fend off brute force registration attempts.

## Slide 4: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
8. Disable channels and services that are not in use
Disable channels that you aren’t using like skinny and MGCP. For Asterisk PBXs, you can “unload” these modules in the /etc/modules.conf file

## Slide 5: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
9. Make it harder for sip scanners (Set “alwaysauthreject=yes” )
Set “alwaysauthreject=yes” in your sip configuration file. What this does is prevent Asterisk from telling a sip scanner which extensions are valid by rejecting authentication requests

## Slide 6: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
…on existing usernames with the same rejection details as with nonexistent usernames. If they can't find you they can't hack you!
Another way to make it hard for SIP scanners is to install a SIP port firewall. This will block

## Slide 7: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
…“scanning” of port 5060 and 5061 and can disable the attempting endpoint for a specific time when it detects a violation.

## Slide 8: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
10. Limit and restrict routing and phone number dial plans
Restrict calling to high-cost calling destination and don’t allow calling to 0900 + Premium numbers)

## Slide 9: CASE STUDY – ASTERISK VOIP SECURITY HARDENING (2)
11. Audit your system security regularly
END