## Slide 1: Case Study Security Hardening – Cisco IOS 15
CIS Benchmarks case study (Cisco IOS 15)
For Cisco routers running IOS 15M

## Slide 2: Case Study Security Hardening – Cisco IOS 15
June 30, 2015
151 pages PDF doc

## Slide 3: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
Profile applicability:
  Level 2

## Slide 4: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Description: Enable Open Shortest Path First (OSPF) Message Digest 5 (MD5) authentication.

## Slide 5: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Rationale: This is part of the OSPF authentication setup

## Slide 6: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Audit: Verify the appropriate md5 key is defined on the appropriate interface(s)
  hostname#sh run int {interface}

## Slide 7: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Remediation: Configure the appropriate interface(s) for Message Digest authentication

## Slide 8: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Remediation:…
  hostname(config)#interface {interface_name} hostname(config-if)#ip ospf message-digest-key {ospf_md5_key-id} md5 {ospf_md5_key}

## Slide 9: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Impact: Organizations should plan and implement enterprise security policies that require rigorous authentication methods for routing protocols…

## Slide 10: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Impact: …Configuring the proper interface(s) for 'ip ospf message-digest-key md5' enforces these policies by restricting exchanges between network devices.

## Slide 11: Case Study Security Hardening – Cisco IOS 15
3.3.2.2 Set 'ip ospf message-digest-key md5' (Scored)
  Default Value: Not set
END